## Slide 1: Programming with CUDA
Section 2

## Slide 2: The CUDA Programming Model

## Slide 3: Overview
Software – driver and runtime APIs
Execution model – kernels, threads, and blocks
Hardware architecture

## Slide 4: Drive API
Low level API
Shipped along with the display driver

## Slide 5: Runtime API
High level API
Included with the CUDA toolkit
Redistribute with your application

## Slide 6: Runtime API Version Must be >= Driver API Version
Notes: Something that needs to grab the viewers attention!!

## Slide 7: Execution Model
Kernel – top-level device function
Executed by N CUDA threads in parallel

## Slide 8: Threads and Blocks
Grid
Block 0
...
Block 0
Thread 0
...
Block 1
Block 2
...
Thread 1
Thread 2
Thread 3
Thread 4

## Slide 9: Hardware Architecture
Streaming multiprocessors (SMs)
SIMT architecture
Hardware multithreading

## Slide 10: Streaming Multiprocessors
Several SMs on each GPU
Multiple CUDA cores per SM
Shared cache, registers, and memory
Global memory shared by all SMs
No branch prediction or speculative execution

## Slide 11: Compute Capability
Version number which identifies general specifications of a CUDA device
Notes: [Mandatory Slide] This would be the introduction slide of the topic that you are covering in this subsection.
When this slide plays, you could talk about the main aim that we’d be covering in this video.

## Slide 12: SIMT Architecture
Single instruction and multiple thread
Unlike SIMD, the width here is variable
Threads have independent states and can diverge

## Slide 13: Warps
Groups of 32 threads, are scheduled, and run as a unit
Notes: Something that needs to grab the viewers attention!!

## Slide 14: Hardware Multithreading
Execution context stays on chip
No overhead for switching warps

## Slide 15: Running a Kernel
Blocks are assigned to available SMs
Blocks are split into warps
Multiple warps/blocks run on each SM
As blocks finish, new blocks are scheduled

## Slide 16: Summary
Looked at driver and runtime APIs
Looked at kernels executed by many threads, and organized into a grid of blocks
Explained SIMT hardware architecture scales to hardware capabilities

## Slide 17: Kernel Execution Configurations
Next Video